## Slide 1
Raspberry PI 3 [Firmware Attestation Trust Client ]
Trust Zone Secure World
Trust Storage
- Arm Chip UDID
- RSA encryption key list
- Attestation result data
Raspbian Normal World
IoT hub communication module
Message decryption function
Arm UDID verification function
Firmware attestation algo function
Result encryption function
IoT data load module
Arm Chip UDID
Encrypted seeds message
FA algo seeds
Firmware program and memory prob module
Mem Addresses
Mem byte data
Firmware
Memory
Encrypted attestation result message
Trust Execution Environment
OPTEE
network
Encrypted Firmware attestation request
Encrypted Firmware attestation result
IoT Device Control Hub
Arm Chip information
TEE verify module
TEE driver
Trust Client Init
Config file

## Slide 2
Client Application
OPTEE trust application [client <-> server ] design(10/07/2019)
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
Pre-stored Value:
AES default Key, AES IV
Challenge String length
SWATT calculation Iteration time [m]
Linear congruential random(BSD rand MAX and seed offset )
File address block range.
Functions:
Accept the trustClient(normal word) connection.
Load default AES-Key, decrypt msg, get session key. => Set AES session key, decrypt msg and get challenge str.
Create first randomSeed and extract challenge string => random file byte’s address + state list.
Do SWATT calculation for input byte, refresh all the TA(trustWorld) inside parameters.
Return to step 3, repeat n times.
Finished all and get the final SWATT int/hex val.
Load AES-session Key, encrypt SWATT value.
Load AES-session -Key, decrypt msg, get server verify result.
TEE driver
1
1, 2, 3, 4, 5, 7
Normal World [Raspbian]
OPTEE driver <=> Tee-supplicant service
1 - Start OPTEE session
Trust Server thread
0 . Init TCP client and load config file
2.2 - Load AES256 key + IV
=> Create random 32B session key => Encrypt session key
2.3 Fetch Pre-saved program
1, 2, 3, 4, 5, 7
2 – Log in to the trust server
Main server start
Load AES256 key + IV
Login request: F;Gateway_ID;Program_V;Key_Version;C_Len, m, n
2.1 confirm log in
2.1.1 Log in reject.
2.4 Calculate the file SWATT
Database
2.3 Forward session key msg to TA(TrustZone)
2
3.1 Load file in memory and fetch bytes based on the Addr
3 x m
Addr
4. Forward new init seed, swat-seed, state[n], file bytes to TA
4 x m
5. Load the encrypted swatt msg
5
5.1 Decrypt the SWATT feed back msg
6. Verify the SWATT value and create the report
6.1. AES Encrypt the SWATT value + verify result
7. Forward encrypted feedback msg
7
7.1 Load verification result
- Verify success => Terminate
- Verify failed => Remove the checked program. ( or return to step 2 )
7.1
NetWork
8. Check the program running status , System library usage and (memory usage ), encrypt message
8. Decrypt the message and save the program running data.
8
Encrypted AES session key
2.3 Session key setup confirm
2.3 Create the random Swatt Challenge string based on the C_len and encrypted the msg.
2.3 Forward challenge string msg to TA
2