## Slide 1
Raspberry PI 3 [Firmware Attestation Trust Client ]
Trust Zone Secure World
Trust Storage
- Arm Chip UDID
- RSA encryption key list
- Attestation result data
Raspbian Normal World
IoT hub communication module
Message decryption function
Arm UDID verification function
Firmware attestation algo function
Result encryption function
IoT data load module
Arm Chip UDID
Encrypted seeds message
FA algo seeds
Firmware program and memory prob module
Mem Addresses
Mem byte data
Firmware
Memory
Encrypted attestation result message
Trust Execution Environment
OPTEE
network
Encrypted Firmware attestation request
Encrypted Firmware attestation result
IoT Device Control Hub
Arm Chip information
TEE verify module
TEE driver
Trust Client Init
Config file

## Slide 2
Raspberry PI 3
IoT sensors
Trust Zone Secure World
Trust Storage
Trust Execution Environment
Trust Execution Environment Driver
Trust Firmware Attestation Client
Trust Client
Target IOT Firmware / Application
Raspbian Normal World
Network
IoT Control Hub
IoT Function Handling Service
Trust Firmware Attestation Service
Normal IoT data communication channel
Encrypted firmware attestation data channel
Database
Cloud Server
Red team attacker
Firmware attack
Red team attacker
Replay attack
TrustZone Protected IoT Device

## Slide 3
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
0. Load config file
1. OPTEE session
TCP Client
Tee-supplicant service
OPTEE driver
2. Accept OPTEE connection
Raspberry PI
Trust Server Computer
3. Accept the TCP connection
Arm Chip information
Config file
Arm Chip UDID
IoT device information
UDID match ?
Device verified
Invalid Device
Yes
No

## Slide 4
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Trust Server Computer
RSA[2048] encryption
OPTEE driver <=> Tee-supplicant service
Communication module
Parse message
Fetch RSA Key based on the IoT information
Decrypt the message, get the Random#1, append Random#2 and PATT parameters
Decrypt the message
RSA[2048] Encryption
2048bits-RSA-key
256bits-Random#1
Verify result
Firmware info
RSA encrypted verification data
2048bits-RSA-key
RSA encrypted firmware attestation request
Forward message to server
Communication module
Forward message to TEE
Verify server response Random#1 correct

## Slide 5
Internet
Trust App [Trust Zone]
Trust Client [Normal world]
Server program
Raspberry PI
Trust Server Computer
Use the PATT to parameters get the random block/bytes memory address/file position.
OPTEE driver <=> Tee-supplicant service
Bytes address
Fetch related bytes data from the address
Fetch the pre-saved Firmware from DB
Encrypt the PATT result, msg Idx, server Random #2
Add bytes to SWATT checksum calculation
Run Firmware in IoT emulation environment and calculate the PATT
Communication module
Finished iteration ?
Bytes data
No
Yes
Decrypt the message to get the Random #2 and PATT value then verify whether both value can match.
RSA encrypted PATT message
Forward message to server

## Slide 6
IoT sensors
TEE driver ready

## Slide 7
Client Application
OPTEE Trust Application [IoT firmware attestation workflow]
Raspberry PI mode 3
Secure World [OPTEE]
Trust Application
TA-UUID[7aaaf200-2450-11e4-abe2-0002a5d5c51b]
Pre-stored Value:
RSA default Key
PATT Challenge String length
PATT calculation Iteration time [m]
Linear congruential random(BSD rand MAX and seed offset )
Raspberry PI Arm Chip UDID
File address block range.
Functions:
Accept the trustClient(normal word) connection.
Load default RSA-Key, decrypt msg, get session key. => Set RSA session key, decrypt msg and get challenge str.
Create first randomSeed and extract challenge string => random file byte’s address + state list.
Do PATT calculation for input byte, refresh all the TA(trustWorld) inside parameters.
Return to step 3, repeat n times.
Finished all and get the final PATT int/hex val.
Load RSA-session Key, encrypt PATT value.
Load RSA-session -Key, decrypt msg, get server verify result.
TEE driver
1
1, 2, 3, 4, 5, 7
Normal World
OPTEE driver <=> Tee-supplicant service
1 - Start OPTEE session
Trust Server thread
0 . Init TCP client and load config file
2.3 Fetch Pre-saved program
1, 2, 3, 4, 5, 7
2 – Log in to the trust server
Main server start
Load AES256 key + IV
Login request: F;Gateway_ID;Program_V;Key_Version;C_Len, m, n
2.1 confirm log in
2.1.1 Log in reject.
2.4 Calculate the filep PATT
Database
2.3 Forward session key msg to TA(TrustZone)
2
3.1 Load file in memory and fetch bytes based on the Addr
3 x m
Addr
4. Forward new init state, Arm UDID, state[n], file bytes to TA
4 x m
5. Load the encrypted PATT parameters msg
5
5.1 Decrypt the PATT result feed back msg
6.1. RSA Encrypt the PATT value + verify result
7. Forward encrypted feedback msg
7
7.1 Load verification result
- Verify success => Terminate
- Verify failed => Remove the checked program. ( or return to step 2 )
7.1
Internet
8. Check the program running status , System library usage and (memory usage ), encrypt message
8. Decrypt the message and save the program running data.
8
2.3 Session key setup confirm
2.3 Create the random PATT Challenge string based on the C_len and encrypted the msg.
2.3 Forward challenge string msg to TA
2
2.2 - Load AES256 key + IV
=> Create random 32B session key => Encrypt session key
6. Verify the PATT value and create the report
Trust Server

## Slide 8
Config.mk:
export CROSS_COMPILE := /path/to/your/linaro/aarch32/bin/arm-linux-gnueabihf-
export CROSS_COMPILE_AARCH64 := /path/to/your/linaro/aarch64/bin/aarch64-linux-gnu-